## Slide 1
Lab: Designing Embedded Application-Specific Processors
Majd Eddin Mansour Paul Georg Wagner
Supervisors: Sajjad Hussain
Dr. Hussam Amrouch

## Slide 2: Outline
Introduction To The Project
  ADPCM Decoder Algorithm
  Simulating and Implementing Steps
  Preparing a Benchmark
Performance Optimized CPUs
Area Optimized CPUs
Conclusion

## Slide 3: ADPCM Algorithm (pseudo code)
static int indexTable[16] = {
-1, -1, -1, -1, 2, 4, 6, 8,
-1, -1, -1, -1, 2, 4, 6, 8,
};
static int stepsizeTable[89] = {
7, 8, 9, 10, 11, 12, 13, 14, 16, 17,
19, 21, 23, 25, 28, 31, 34, 37, 41, 45,
50, 55, 60, 66, 73, 80, 88, 97, 107, 118,
130, 143, 157, 173, 190, 209, 230, 253, 279, 307,
337, 371, 408, 449, 494, 544, 598, 658, 724, 796,
876, 963, 1060, 1166, 1282, 1411, 1552, 1707, 1878, 2066,
2272, 2499, 2749, 3024, 3327, 3660, 4026, 4428, 4871, 5358,
5894, 6484, 7132, 7845, 8630, 9493, 10442, 11487, 12635, 13899,
15289, 16818, 18500, 20350, 22385, 24623, 27086, 29794, 32767
};

## Slide 4: ADPCM Algorithm (pseudo code)
int adpcm_decoder(unsigned char* indata, int len) {
for ( ; len > 0 ; len-- ) {
} }
/* Step 1 - get the delta value */
if ( bufferstep ) {
delta = inputbuffer & 0xf;
} else {
  inputbuffer = *indata++;
  delta = (inputbuffer >> 4) & 0xf;
}
bufferstep = !bufferstep;
/* Step 2 - Find new index value (for later) */
step = stepsizeTable[index];
index += indexTable[delta];
if ( index < 0 ) index = 0;
if ( index > 88 ) index = 88;
/* Step 3 - Separate sign and magnitude */
sign = delta & 8;
delta = delta & 7;
/* Step 4 - difference and new predicted value */
vpdiff = step >> 3;
if ( delta & 4 ) vpdiff += step;
if ( delta & 2 ) vpdiff += step>>1;
if ( delta & 1 ) vpdiff += step>>2;
if ( sign )
valpred -= vpdiff;
else
valpred += vpdiff;
/* Step 5 - clamp output value */
if ( valpred > 32767 )
valpred = 32767;
else if ( valpred < -32768 )
valpred = -32768;

## Slide 5: Simulating ADPCM
Application compiled with gcc and executed
Converted to assembly:
  To understand the instructions used for the decoder
  Easier to replace group of instructions with new instructions
  Very helpful in area optimizing to find out the unneeded components
Simulated with dlxsim and ModelSim
  Using the unmodified CPU
The output correctness is verified by comparing results

## Slide 6: Implementing ADPCM
CPU with App loaded to the FPGA and simulated
  Bitrate in dlx_Toplevel.vhd set to 96 kHz audio
  A bitstream is generated using Xilinx ISE for dlx_basis CPU
  The bitstream is initialized with the application and uploaded
As a result we could hear the decoded output by the FPGA
  Very slow playback at 25, 50, 75 MHz
  Yet slow playback at 100 MHz (deep sound)
Sound is encoded with 192 kHz instead of 96 kHz
  We resampled the provided audio data by decoding the sound and re-encoding it with 96 kHz

## Slide 7: Preparing a Benchmark
The output and the function calling are removed from adpcm.c
  The provided adpcmDataStereo_MINI.h is linked
  Converted to Assembly
Simulated with ModelSim to record the count of cycles
  (CLK_HALF_PERIOD = 10ns // 50 MHz)
Area and timing reports are generated the using Xilinx ISE
  Synthesized VHDL files + benchmark framework are loaded
Power benchmark with Xilinx ISE
  After creating VCD files using ModelSim

## Slide 8: Benchmark Results (Basis CPU)
Cycles | 388.814
(Maximum)
Chart: LUTs (3260)
| 1st Qtr
LUT | 4.7164 | 95.2836
Chart: Slices (998)
| 1st Qtr
LUT | 5.7755 | 94.2245
Critical path [ns] | 6,316

## Slide 9: Benchmark Results (Basis CPU)
Chart: Power [mW]
| 50 MHz | 158 MHz | 29 MHz
Leakage power | 1043 | 1044 | 1043
Dynamic Power | 50 | 99 | 37
Energy | 8.5 | 2.81 | 14.48
Execution Time [ms] | 7,78 | 2,46 | 13,41

## Slide 10: PERFORMANCE optimization

## Slide 11: Performance Optimization
Goal: Minimizing the execution time
Reduce number of cycles
  Optimize existing code
  Create suitable hardware components/instructions
  Enhance data parallelism
Convert project to assembly to allow finer control
  Main point of optimization: for-loop

## Slide 12: Performance Optimization 1
Outsourcing index and step calculation to hardware
  New VHDL component
  Saves two address calculations/memory accesses
  Saves two if-statements
Notes: - Arrays defined in VHDL
- No need for a clamp instruction, just add clamping to the actually important component

## Slide 13: Performance Optimization 1
VHDL implementation of lstep and addidx instruction
  Input: sample, old index
  Output: step, new index
Notes: - Arrays defined in VHDL
- No need for a clamp instruction, just add clamping to the actually important component
13

## Slide 14: Performance Optimization 1
Loading two samples at once
  Load one byte
  Store two samples in two registers
  No new VHDL component required
Also process two samples in one loop iteration
Notes: Enables us to process two samples in one loop iteration
  => Data parallelism
14

## Slide 15: Performance Optimization 1
Outsource PCM decoding to hardware
  Input: Sample (r3), Step (r5), Previously decoded sample (r10)
  Output: Decoded sample (r9)
Notes: 15

## Slide 16: Performance Optimization 1
VHDL implementation of pcmdec instruction
Notes: - Clamping omitted
16

## Slide 17: Performance Optimization 1
Optimized code inside the for-loop
Notes: - Registers r8 and r10 are preserved over the iterations (they hold old index and old decoded sample)
17

## Slide 18: Performance Optimization 1: Results – Execution Time
Chart: Execution time [ms]
| 50 MHz (basis) | 50 MHz (opt1) | 158 MHz (basis) | 130 MHz (opt1) | 29 MHz (basis) | 2,7 MHz (opt1)
Execution time | 7.78 | 0.73 | 2.46 | 0.28 | 13.41 | 13.5
# Cycles basis | 388.814
# Cycles opt1 | 36.462
Speedup | 10,7
Notes: Speedup of 10,7
This is paid for by higher area requirements (about 50% more)
And of course higher power requirements

## Slide 19: Performance Optimization 1: Results – Power & Energy
Chart: Power [mW]
| 50 MHz (basis) | 50 MHz (opt1) | 158 MHz (basis) | 130 MHz (opt1) | 29 MHz (basis) | 2,7 MHz (opt1)
Leakage Power | 1043 | 1043 | 1044 | 1044 | 1043 | 1043
Dynamic Power | 50 | 59 | 99 | 116 | 37 | 23
Energy | 8.5 | 0.8 | 2.81 | 0.33 | 14.48 | 14.4

## Slide 20: Performance Optimization 1: Results – Area
Chart: LUTs (3260)
| 1st Qtr
LUT | 4.7164 | 95.2836
Chart: Slices (998)
| 1st Qtr
LUT | 5.7755 | 94.2245
Chart: LUTs (4853)
| 1st Qtr
LUT | 7.0211 | 92.9789
Chart: Slices (1602)
| 1st Qtr
LUT | 9.2708 | 90.7292
basis:
opt1:
Notes: Area requirement increased by about 50%

## Slide 21: Performance Optimization 2
Reducing number of components to just one
  Step calculation and decoding of two samples is done in a single component
Advantages
  Reduced number of instructions
  Code inside the for-loop becomes very simple
Notes: - New pcm instruction
- Inputs: Two input samples (r3 and r4), step (r5) and previously decoded sample (r6)
- Outputs: Two output samples (r3 and r4), new step (r5) and secondly decoded sample (r6)
21

## Slide 22: Performance Optimization 2: Results – Execution Time
Chart: Execution time [ms]
| 50 MHz (basis) | 50 MHz (opt2) | 158 MHz (basis) | 154 MHz (opt2) | 29 MHz (basis) | 1,3 MHz (opt2)
Execution time | 7.78 | 0.37 | 2.46 | 0.12 | 13.41 | 14.04
# Cycles basis | 388.814
# Cycles opt2 | 18.258
Speedup | 21,3
Notes: Speedup doubles (mostly due to the decreased number of instructions)
Interestingly: Critical path gets shorter => Probably because we do not use multiple components in a single cycle anymore
Area decreases only marginally

## Slide 23: Performance Optimization 2: Results – Power & Energy
Chart: Power [mW]
| 50 MHz (basis) | 50 MHz (opt2) | 158 MHz (basis) | 154 MHz (opt2) | 29 MHz (basis) | 1,3 MHz (opt2)
Leakage Power | 1043 | 1043 | 1044 | 1044 | 1043 | 1043
Dynamic Power | 50 | 59 | 99 | 117 | 37 | 21
Energy | 8.5 | 0.4 | 2.81 | 0.14 | 14.48 | 14.94
Notes: Dynamic power increased only marginally
Nevertheless energy requirement decreased significantly, because of lower execution time

## Slide 24: Performance Optimization 2: Results – Area
basis:
opt2:
Chart: LUTs (3260)
| 1st Qtr
LUT | 4.7164 | 95.2836
Chart: Slices (998)
| 1st Qtr
LUT | 5.7755 | 94.2245
Chart: LUTs (4827)
| 1st Qtr
LUT | 6.9835 | 93.0165
Chart: Slices (1550)
| 1st Qtr
LUT | 8.9699 | 91.0301
Notes: Marginally less area than before

## Slide 25: Performance Optimization 3
Increase the number of samples decoded in one step
  Currently: two output registers holding two decoded samples
  In each register two 16-bit output samples can be stored
  Goal: decode four samples with one instruction
New load instruction loads four input samples
  Also increases address register
Notes: - New pcm instruction
- Inputs: Two input samples (r3 and r4), step (r5) and previously decoded sample (r6)
- Outputs: Two output samples (r3 and r4), new step (r5) and secondly decoded sample (r6)
25

## Slide 26: Performance Optimization 3: Results – Execution Time
Chart: Execution time [ms]
| 50 MHz (basis) | 50 MHz (opt3) | 158 MHz (basis) | 124 MHz (opt3) | 29 MHz (basis) | 0,5 MHz (opt3)
Execution time | 7.78 | 0.13 | 2.46 | 0.05 | 13.41 | 13.11
# Cycles basis | 388.814
# Cycles opt3 | 6.554
Speedup | 59,3

## Slide 27: Performance Optimization 3: Results – Power & Energy
Chart: Power [mW]
| 50 MHz (basis) | 50 MHz (opt3) | 158 MHz (basis) | 124 MHz (opt3) | 29 MHz (basis) | 0,5 MHz (opt3)
Leakage Power | 1043 | 1043 | 1044 | 1044 | 1043 | 1043
Dynamic Power | 50 | 67 | 99 | 132 | 37 | 24
Energy | 8.5 | 0.15 | 2.81 | 0.06 | 14.48 | 13.99

## Slide 28: Performance Optimization 3: Results – Area
basis:
opt3:
Chart: LUTs (3260)
| 1st Qtr
LUT | 4.7164 | 95.2836
Chart: Slices (998)
| 1st Qtr
LUT | 5.7755 | 94.2245
Chart: LUTs (5883)
| 1st Qtr
LUT | 8.5113 | 91.4887
Chart: Slices (2015)
| 1st Qtr
LUT | 11.6609 | 88.3391
Notes: Another increase by about 25% compared to the previous version.

## Slide 29: Performance Optimization: Problems
Constrained number of operand registers
  With 32 bit long instruction words, 6 bit opcode and 5 bit register addresses, only 5 register operands are supported
  Used operand registers for input and output simultaneously
  Unproblematic due to pipeline structure
Standard register file only supports a maximum of 4 read and 4 write ports
  Data parallelism requires storing of multiple samples in one register
  Theoretical limit: 7 output samples written in one instruction
  The third optimized CPU supports a maximum of 4 output samples
Notes: 29

## Slide 30: Performance Optimization 3: Overall Speedup
Chart: Speedup of Performance Optimized CPUs at 50 MHz
| basis | opt1 | opt2 | opt3
Execution time | 7.78 | 0.73 | 0.37 | 0.13
Speedup | 1 | 10.7 | 21.3 | 59.3

## Slide 31: Area optimization

## Slide 32: Area Optimization
Goal: Reducing the needed slices and LUTs
Method: Using as few components as possible
  By simply removing as many hardware resources as possible from the CPU description

## Slide 33: Area Optimization 1
The MUL0 and DIV0 resources are removed from the CPU
  Along with the instructions that use these resources
The size of the register file is reduced from 32 to only 16 registers.
  Registers are addressed using only 4 bits instead of 5 bits.
    The micro operations which use the register address is modified
    In those macros we simply removed the most significant bit before calling GPR.read() or GPR.write() with a register address
  The dedicated link register, and hence the jal, jalr, and jr instructions are removed

## Slide 34: Area Optimization 1: Results - Slices, LUTs
Chart: Number of Slices/LUTs
| Basis | Area Opt1
Slices | 998 | 510
LUTs | 3260 | 1661
Cycles | 388418 | 202481
(5%)
(2,4%)
(6%)
(3%)

## Slide 35: Area Optimization 2
Yet more registers are removed from the register file
Registers are generalized and reused as much as possible
  For example, in each iteration the base address of the input sample array has to be reloaded
The code is re-implemented in order to use only seven registers
This increases the number of required instruction cycles, and hence the execution time

## Slide 36: Area Optimization 2: Results - Slices, LUTs
Chart: Number of Slices/LUTs
| basis | area_opt1 | area_opt2
Slices | 998 | 510 | 437
LUTs | 3260 | 1661 | 1203
Cycles | 388418 | 202481 | 239506
(5%)
(6%)
(2,4%)
(3%)
(1,7%)
(2,5%)

## Slide 37: Area Optimization: Results – Power & Energy
Chart: Power [mW]
| 50 MHz (basis) | 50 MHz (area_opt1) | 50 MHz (area_opt2)
Leakage power | 1043 | 1043 | 1043
Dynamic Power | 50 | 49 | 41
Energy | 8.5 | 4.42 | 5.19
Execution Time [ms] | 7,78 | 4,05 | 4,79

## Slide 38: Area Optimization: Problems
As we used the registers (from r0 to r7), r0 could not be used as a general purpose register.
  Could be hardware coded
After re-implementing the code for the second optmization, it was not feasable to debug with dlxsim
  Dlxsim shows correct results, but ModelSim does not

## Slide 39: Conclusion
Optimizing performance can be applied on costs of either power and energy or area
  In our project the performance optimization caused a small loss of area
Optimizing area can be applied on costs of performance, power or energy

## Slide 40: Appendix: Benchmark Results
Basis CPU
Performance Optimized Version 1

## Slide 41: Appendix: Benchmark Results
Performance Optimized Version 2
Performance Optimized Version 3

## Slide 42: Appendix: Benchmark Results
Area Optimized Version 1
Area Optimized Version 2