ADPCM ASIPs
Nitzsche, Pachideh - Group 02

---
Analysis of the Basis CPU
Nitzsche, Pachideh – Group 02

---
Analysis of the Basis CPU
Measurement as per chapter 6.4
ASIPMeister HDL files with benchmark framework
Standard ISE configuration
Area Report
998 Slices
3260 Slice LUTs
Timing Report
Critical path of 6.316ns
Max. frequency of 158.328MHz
[Speaker Notes: The outline is just an and has to be adjusted example (see https://sdqweb.ipd.kit.edu/wiki/Vortragshinweise) and copied to each slide manually. The current chapter should be in bold font. The distance of the words can be adjusted automatically by PowerPoint: select all words and arrows and then select “Anordnen -> Ausrichten -> Horizontal verteilen” (PowerPoint2007). Prof. Dr. Max Mustermann | Name of Faculty]

---
Area - Optimized Processor
16 Register GPR
Reduced Instruction Set and Hardware Resources
Custom ADPCM Application

---
Area: General Approach
Exploring ASIPMeister’s functionalities
(Design priority from “Performance” to “Area”)
Using the built-in estimation system to decide on the meaningfulness of design changes, e.g.
GPR read ports from 2 to 1: saves	5000 gates
Replacing all jumps with rel. jumps:	500 gates
Reducing ISA to 16bit:	10000+ gates
GPR registers from 32 to 16:	17000 gates
[Speaker Notes: The outline is just an and has to be adjusted example (see https://sdqweb.ipd.kit.edu/wiki/Vortragshinweise) and copied to each slide manually. The current chapter should be in bold font. The distance of the words can be adjusted automatically by PowerPoint: select all words and arrows and then select “Anordnen -> Ausrichten -> Horizontal verteilen” (PowerPoint2007). Prof. Dr. Max Mustermann | Name of Faculty]

---
Area: General Approach
Xilinx ISE configuration
Design Strategy “Area Reduction with Physical Synthesis” applied
Automatically configures design modes and effort levels throughout all stages of synthesis
[Speaker Notes: The outline is just an and has to be adjusted example (see https://sdqweb.ipd.kit.edu/wiki/Vortragshinweise) and copied to each slide manually. The current chapter should be in bold font. The distance of the words can be adjusted automatically by PowerPoint: select all words and arrows and then select “Anordnen -> Ausrichten -> Horizontal verteilen” (PowerPoint2007). Prof. Dr. Max Mustermann | Name of Faculty]

---
Area: Stripping the CPU
The GPR’s register set was reduced from 32 to 16 registers (32bit)
Custom register file specification
Changes to all instruction types
Adjustments to some Micro Op. Descriptions
Removal of all instructions, that weren’t used by the -O3 compiled application
29 instructions removed
MUL and DIV resources removed
[Speaker Notes: The outline is just an and has to be adjusted example (see https://sdqweb.ipd.kit.edu/wiki/Vortragshinweise) and copied to each slide manually. The current chapter should be in bold font. The distance of the words can be adjusted automatically by PowerPoint: select all words and arrows and then select “Anordnen -> Ausrichten -> Horizontal verteilen” (PowerPoint2007). Prof. Dr. Max Mustermann | Name of Faculty]

---
Area: Generating the application
Manual overhaul of the assembly code was infeasible
→compiler needed
Changes while working with the CoSy makescripts:
Startup script support for new special registers
Debugging files that are generated on i80pc06
Final touches to the generated code
Removal of NOPs
Fixed compiler bug: zero-register wasn’t used for initializations
[Speaker Notes: The outline is just an and has to be adjusted example (see https://sdqweb.ipd.kit.edu/wiki/Vortragshinweise) and copied to each slide manually. The current chapter should be in bold font. The distance of the words can be adjusted automatically by PowerPoint: select all words and arrows and then select “Anordnen -> Ausrichten -> Horizontal verteilen” (PowerPoint2007). Prof. Dr. Max Mustermann | Name of Faculty]

---
Speed - Optimized Processor
Custom Instructions
Custom Instructions
Custom Instructions
(and some code optimizations)

---
Speed: Choosing custom instructions
Finding bottlesnecks
Rate capabilities of hardware
Add some required hardware
Implement custom instructions
→Goal: One instruction per ADPCM step
[Speaker Notes: The outline is just an and has to be adjusted example (see https://sdqweb.ipd.kit.edu/wiki/Vortragshinweise) and copied to each slide manually. The current chapter should be in bold font. The distance of the words can be adjusted automatically by PowerPoint: select all words and arrows and then select “Anordnen -> Ausrichten -> Horizontal verteilen” (PowerPoint2007). Prof. Dr. Max Mustermann | Name of Faculty]

---
Speed: Finding bottlenecks
Estimated required cycles per ADPCM step
e.g. Step 1 needed about 200 cycles
Large amount of cycles for if/else commands
Partly due to strange compiler decisions
[Speaker Notes: The outline is just an and has to be adjusted example (see https://sdqweb.ipd.kit.edu/wiki/Vortragshinweise) and copied to each slide manually. The current chapter should be in bold font. The distance of the words can be adjusted automatically by PowerPoint: select all words and arrows and then select “Anordnen -> Ausrichten -> Horizontal verteilen” (PowerPoint2007). Prof. Dr. Max Mustermann | Name of Faculty]

---
Speed: Is the CoSy Compiler crazy?
if ( index > 88 )
[Speaker Notes: The outline is just an and has to be adjusted example (see https://sdqweb.ipd.kit.edu/wiki/Vortragshinweise) and copied to each slide manually. The current chapter should be in bold font. The distance of the words can be adjusted automatically by PowerPoint: select all words and arrows and then select “Anordnen -> Ausrichten -> Horizontal verteilen” (PowerPoint2007). Prof. Dr. Max Mustermann | Name of Faculty]

---
Speed: Possible Custom Instructions
delta(inputbuffer, indata, bufferstep)
clamp(index, 0, 88)
vpd(vpdiff, delta, step)
vpd(vpdiff, delta, step)
sgn(sign, valpred, vpdiff)
clamp(index, 1, 32767)
[Speaker Notes: The outline is just an and has to be adjusted example (see https://sdqweb.ipd.kit.edu/wiki/Vortragshinweise) and copied to each slide manually. The current chapter should be in bold font. The distance of the words can be adjusted automatically by PowerPoint: select all words and arrows and then select “Anordnen -> Ausrichten -> Horizontal verteilen” (PowerPoint2007). Prof. Dr. Max Mustermann | Name of Faculty]

---
Speed: The clamp-Instruction
clamp(index, 0, 88)
clamp(index, 1, 32767)
[Speaker Notes: The outline is just an and has to be adjusted example (see https://sdqweb.ipd.kit.edu/wiki/Vortragshinweise) and copied to each slide manually. The current chapter should be in bold font. The distance of the words can be adjusted automatically by PowerPoint: select all words and arrows and then select “Anordnen -> Ausrichten -> Horizontal verteilen” (PowerPoint2007). Prof. Dr. Max Mustermann | Name of Faculty]

---
Benchmark Results

---
Benchmark Results Part 2
CPU	@50MHh			@max.			@min.
	time / [ms]	power / [mW]	Energy / [uJ]	time / [ms]	power / [mW]	Energy / [uJ]	time / [ms]	power / [mW]	Energy / [uJ]
basis	8.74	52	454.5	2.77	127	351.8	5.16	76	392.2
area	5.84	55	321.2	2.05	134	274.4	6.34	51	323.3
speed	1.52	103	156.6	0.63	220	138.6	6.09	41	249.7
[Speaker Notes: The outline is just an and has to be adjusted example (see https://sdqweb.ipd.kit.edu/wiki/Vortragshinweise) and copied to each slide manually. The current chapter should be in bold font. The distance of the words can be adjusted automatically by PowerPoint: select all words and arrows and then select “Anordnen -> Ausrichten -> Horizontal verteilen” (PowerPoint2007). Prof. Dr. Max Mustermann | Name of Faculty]

---
Benchmark Results Part 1
CPU	area / [LUTs]	cr. path / [ns]	max. freq. / [MHz]	cycles	min. freq. / [MHz]
basis	3260	6.316	158.328	436k	84.5
area	1259	7.02	142.45	291k	46
speed	4756	8.307	120.38	76k	12.5
[Speaker Notes: The outline is just an and has to be adjusted example (see https://sdqweb.ipd.kit.edu/wiki/Vortragshinweise) and copied to each slide manually. The current chapter should be in bold font. The distance of the words can be adjusted automatically by PowerPoint: select all words and arrows and then select “Anordnen -> Ausrichten -> Horizontal verteilen” (PowerPoint2007). Prof. Dr. Max Mustermann | Name of Faculty]

---
Benchmark Results Part 2
CPU	@50MHh			@max.			@min.
	time / [ms]	power / [mW]	Energy / [uJ]	time / [ms]	power / [mW]	Energy / [uJ]	time / [ms]	power / [mW]	Energy / [uJ]
basis	8.74	52	454.5	2.77	127	351.8	5.16	76	392.2
area	5.84	55	321.2	2.05	134	274.4	6.34	51	323.3
speed	1.52	103	156.6	0.63	220	138.6	6.09	41	249.7
[Speaker Notes: The outline is just an and has to be adjusted example (see https://sdqweb.ipd.kit.edu/wiki/Vortragshinweise) and copied to each slide manually. The current chapter should be in bold font. The distance of the words can be adjusted automatically by PowerPoint: select all words and arrows and then select “Anordnen -> Ausrichten -> Horizontal verteilen” (PowerPoint2007). Prof. Dr. Max Mustermann | Name of Faculty]

---
Is it over yet?
Thanks for your attention!